## Slide 1: Project ASTRA – Asset Tracking for hospitals Final Presentation
Abhishek Sunkum Rammurthy
Pramod Tikare Muralidhara
Yadhunandana Rajatadripura

## Slide 2: Agenda
Motivation and Objective.
Overview of the architecture and features
Routing protocol – How?
Application
GUI and Targeted outcomes
Future improvements.

## Slide 3: Motivation, Objective
An average hospital can lose $4,000 per day in lost wages due to time spent searching for mobile medical equipment, not to mention the over-procurement of assets to ensure availability - Versus [1]
Motivation
  To track mobile medical equipments in the hospitals
  Increased patient volume, increased health care devices which are prone to misplacements by humans.
  Misplacements, time to track, central inventory management(out of date, over ordering, needs maintenance or disposal).
State of the Art
  WSN to track the assets/devices – Zigbee, BLE, RFID etc
  Lack of standardization, Expensive etc,.
Objective
  To implement a homogenous, scalable real time asset tracking system for hospitals by constructing an efficient, minimum hop energy aware Routing algorithm.
Notes: Motivation
Background
Problems
Solutions and approaches

## Slide 4: Overview
Approach
  2 beacon motes and 6 tracking motes with one being the center mote.
  Application has 2 modes of operation
    Neighbour discovery and maintain routing table with number of hops to Gateway.
    Asset tracking – Time driven beacon information to the center mote.
Routing protocol
  Adhoc distance vector Routing for minimum cost path.
  Cost is the combination of hopcount and available battery life.
Sensors and Actuators
  Battery level sensing – Periodic ADC read
    Button to emulate Battery drain.
  Sounder – Asset out of the network.
  LEDs – Routing path.
Topology Features
  Self organization – Adding new nodes to the network
  Failure Recovery - Node failure in the path - Inform the neighbour. Table updated at the neghnours.
  Dynamic topology – Update Routing tables with change in cost.

## Slide 5: Routing Protocol – How?
Flowchart
Features - Technically

## Slide 6: Application – How?
Path of the asset
Dynamic Routing
  Change is asset location
Impact of battery life -

## Slide 7: GUI and targeted Demo
All the nodes are positioned on the widget. Address of each node is displayed besides the node.
Routing Table of one of the nodes in a message box.
Routing path - Path of the asset location. Asset assigned to one of the nearest nodes.
Dynamic routing - Change in path due to
  Change in asset location.
  Node failure - Failure along the path.
Battery sensing - Battery level of nodes
Actuation - Asset out of the network

## Slide 8: Room for improvements
Correlation between available Battery life and dynamic cost assignment.
RSSI filtering.
  Example – Kalman Filter.
Localization and Indoor positioning.

## Slide 9: Architecture/ Working – Table driven Energy aware Routing
Center node A
Asset 1
Asset 2
NODE C | 
Neighbour | Hops to A
B | 2
D | 3
B
D
F
E

## Slide 10: Architecture/ Working – Table driven Energy aware Routing
Center node A
Asset 1
Asset 2
B
D
F
E
Updated table
Try to reconnect after a timeout/ Neighbor list empty
NODE C | 
Neighbour | Hops to A
D | 3
B | 32

## Slide 11
Questions?

## Slide 12: References
[1] http://www.versustech.com/rtls-solutions/asset-tracking-healthcare-hospital/
[2] Asset Management - Manage and protect valuable mobile medical equipment with the ultimate location platform by Centrak
[3] J.-E. Garcia et all - A Novel DSR-based Energy-efficient Routing Algorithm for Mobile Ad-hoc Networks.
  Gradually increase the forwarding time in relation to the lifetime.
  In our network, gradually increase the HOP information relative to the lifetime.

## Slide 13: Timeplan